## Slide 1: ORBITS IN GNSS
ASEN 5090
ASEN 5090 LECTURE NOTES – LARSON, AXELRAD

## Slide 2: Outline
Kepler’s Laws: 2-body motion
Orbital Elements
GPS Constellation
Orbital Perturbations
GPS Broadcast Ephemeris
Azimuth/Elevation Review
Visibility Software

## Slide 3: KEPLER’S LAWS
Describe motion of an object under a central force
Planets take the path of an ellipse, with the Sun at one focus.
The line joining the planet to the sun sweeps out equal areas in equal times.
The square of the orbital period is proportional to the cube of its mean distance to the sun.
Planet’s Orbit

## Slide 4: KEPLERIAN ORBITAL ELEMENTS

## Slide 5: KEPLERIAN ELEMENTS: SIZE & SHAPE
Central Body
Satellite Location

## Slide 6
KEPLERIAN ELEMENTS:
ORIENTATION

## Slide 7: KEPLERIAN ORBITAL ELEMENTS
Size and shape of the orbit:
Orientation of the orbit:
Position within the orbit (pick one):

## Slide 8: KEPLER’S EQUATION
Center
Earth
Periapsis
Elliptical Orbit
Auxiliary Circle
Satellite Location

## Slide 9: POSITION WITHIN ORBIT PLANE
Solve Kepler’s equation for E iteratively
Then compute the true anomaly
And the distance from the focus

## Slide 10: GPS CONSTELLATION

## Slide 11: CONSTELLATION
32 active satellites
6 orbital planes
5-6 slots per plane

## Slide 12: NOMINAL GPS 24-SATELLITE CONSTELLATION
Semimajor axis = 26559.7 km, inclination = 55 deg, eccentricity = 0
Slot | RAAN (deg) | Argument of Latitude (deg) | Slot | RAAN (deg) | Argument of Latitude (deg)
A1 | 272.847 | 268.126 | D1 | 92.847 | 135.226
A2 | 272.847 | 161.786 | D2 | 92.847 | 265.446
A3 | 272.847 | 11.676 | D3 | 92.847 | 35.136
A4 | 272.847 | 41.806 | D4 | 92.847 | 167.356
B1 | 332.847 | 80.956 | E1 | 152.847 | 197.046
B2 | 332.847 | 173.336 | E2 | 152.847 | 302.596
B3 | 332.847 | 309.976 | E3 | 152.847 | 66.066
B4 | 332.847 | 204.376 | E4 | 152.847 | 333.686
C1 | 32.847 | 111.876 | F1 | 212.847 | 238.886
C2 | 32.847 | 11.796 | F2 | 212.847 | 345.226
C3 | 32.847 | 339.666 | F3 | 212.847 | 105.206
C4 | 32.847 | 241.556 | F4 | 212.847 | 135.346
Defined Epoch: 0000Z, 1 July 1993; Greenwich Hour Angle: 18 h 36 min 14.4 s referenced to FK5/J2000.00 coordinates

## Slide 13: CURRENT CONSTELLATION STATUS
http://www.navcen.uscg.gov/?Do=constellationStatus

## Slide 14: PERTURBATIONS

## Slide 15: ORBITAL PERTURBATIONS FOR THE GPS ORBIT (central force is ~0.5 m/s2)
Source | Acceleration m/s2 | Perturbation | Type
Earth oblateness (J2 ) | 5 x 10-5 | 2 km @ 3 hrs | secular + 6 hr
Sun & moon | 5 x 10-6 | 5-150 m @ 3 hrs | secular + 12hr
Higher Harmonics | 3 x 10-7 | 5-80 m @ 3 hrs | Various
Solar radiation pressure | 1 x 10-7 | 100-800 m @2 days | Secular + 3 hr
Ocean & earth tides | 1 x 10-9 | 0-2m @2 days | secular + 12hr
Earth albedo pressure | 1 x 10-9 | 1-1.5m @2 days | 

## Slide 16: GPS BROADCAST EPHEMERIS

## Slide 17: GPS SATELLITE ORBIT DETERMINATION
Control segment collects range measurements at monitoring stations
Uses precise orbit determination software including high-fidelity models of perturbations to estimate position and velocity (and clocks and many other parameters) of the satellites
Representation of the orbit in the broadcast message is a quasi-Keplerian parameterization that fits best over a 2 hour segment
  toe – time of ephemeris, IODE – issue of data ephemeris
  Keplerian elements
  2 drift rates & Dn
  6 coefficients for harmonic corrections

## Slide 18: BROADCAST EPHEMERIS
M0 Mean anomaly at reference time
Δn Mean motion difference
√a Square root of semi-major axis
Ω0 Longitude of ascending node at weekly epoch
I0 Inclination angle at reference time
ω Argument of perigee
Ω Rate of right ascension
e Eccentricity
IDOT Rate of inclination angle
Cuc Cosine term, argument of latitude
Crc Cosine term, radius
Cic Cosine term, inclination
Cus Sine term, argument of latitude
Crs Sine term, radius
Cis Sine term, inclination
toe Ephemeris reference time
.

## Slide 19
WGS84 (GPS) gravitational parameter for GPS ephemeris users
WGS84 (GPS) earth rotation rate
Computed mean motion
Time from reference epoch (seconds)
Corrected mean motion
Mean anomaly
Kepler’s Equation
True anomaly
Argument of latitude
Argument of latitude correction
Radius correction
Inclination correction
Corrected argument of latitude
Corrected radius
Corrected Inclination

## Slide 20
Earth-fixed coordinates (ECEF):
Positions in orbital plane:
Corrected longitude of ascending node:
ECEF GPS SATELLITE POSITION

## Slide 21: GPS DISPOSAL ORBITS
Satellites no longer actively transmitting are transitioned to LADO (Launch and disposal operations) system
When a GPS satellite is no longer useful it is boosted to a disposal/parking orbit 500 km above the constellation
Over long term, resonance effects of sun, moon produce an increase in eccentricity which causes satellites to cross through operational constellations
Recommendation was made to carefully circularize satellite orbits after boosting to disposal orbit but there are logistics issues with how much fuel is left and what to do with it.
Simulations* show that non-operational GLONASS satellites will cross the GPS operational altitude within 40 years.
*C.C. Chao, R.A. Gick, “Long-term evolution of navigation satellite orbits: GPS/GLONASS/GALILEO,” Advances in Space Research, 34 (2004) 1221-1226

## Slide 22: VISIBILITY (AZIMUTH-ELEVATION)

## Slide 23: AZIMUTH AND ELEVATION
Azimuth (az): angular measure clockwise from North direction to the horizon pierce point
Elevation (el): angular measure from horizon to line-of-sight (LOS) to the object
Satellite
Observer
North
East
Up

## Slide 24: VISIBILITY
LOS is a unit vector pointing
from the user location to the satellite
How do you decide if a satellite is visible?
Compute elevation and azimuth
Satellite position vector in ECEF
User position vector in ECEF

## Slide 25: VISIBILITY SOFTWARE

## Slide 26
VISIBILITY GUI
Time Information
Simulation start time
  Time zone options are available for more intuitive analysis in your local time zone
Duration
Time step

## Slide 27
VISIBILITY GUI
GPS Ephemeris File
YUMA or Broadcast available
  YUMA: slightly faster and more accurate for longer timespans
  Broadcast: very accurate for times near ephemeris epochs
Automatic filename generation
  YUMA source: CelesTrak
  Broadcast source: IGS
Automatic file download

## Slide 28
VISIBILITY GUI
User Location
Latitude, Longitude, Height of user
Ability to store frequent locations in the “My_Places.txt” file
Ellipsoidal height or height above Mean Sea Level (MSL)

## Slide 29
VISIBILITY GUI
Antenna Settings
Pointing direction of antenna
  e.g. 90 el = straight up
  e.g. 0 az, 0 el = north and level
Antenna elevation mask
  Elevation mask for the antenna only. Based on local horizontal of antenna itself
Topocentric elevation mask
  Elevation mask based on local horizon of location

## Slide 30
ELEVATION MASKS
Horizon
Topocentric Elevation Mask
Antenna Elevation Mask
Visible Region

## Slide 31
VISIBILITY RESULTS

## Slide 32
VISIBILITY RESULTS