## Slide 1: IONOSPHERIC EFFECTS ON GNSS
ASEN 5090 Lecture 13
ASEN 5090 LECTURE NOTES – LARSON, AXELRAD

## Slide 2: Homework4 Comments
If possible, take photos!
Write down enough so that someone else should be able to repeat what you did.
Use the visibility code to look at the expected satellite geometry
Provide quantitative results.
Abstract should be a summary of the report – objectives, what you actually did, key results, key conclusions. Keep it short and direct. For these reports, 5 sentences should be about right.
Conclusions should describe what you learned from the experiment. How did the results compare with what you expected? What was surprising?
Recommendations should provide 1) advice to me on how to improve the assignment and 2) advice to hypothetical future students as to what you would do differently if repeating this exercise.
2

## Slide 3: Measurements in your RINEX file
L1 pseudorange –called C1 or P1
L2 pseudorange – P2 or C2
L1 Phase
L2 Phase
Doppler - boring
Signal to noise ratio (SNR) – interesting, but not for this class
L5 phase and pseudorange – not used in this class
(At least) Two kinds of RINEX files

## Slide 4
Homework 5

## Slide 5
Homework 6

## Slide 6: Outline
Characteristics of the Ionosphere
Effect on GPS Observations – code delay, phase advance
Total Electron Content (TEC) & Vertical TEC
Maps
Determining DIr
Ionosphere free pseudorange
Klobuchar model
WAAS model

## Slide 7: Characteristics of the Ionosphere
From Wikipedia article on ionosphere
Ionosphere causes the E-field polarization to rotate, delays the code (modulation), and advances the carrier phase

## Slide 8: IONOSPHERE
From Misra & Enge
Total Electron Content (TEC) is the number of electrons along the signal path
1016 electrons/m² = 1 TEC unit (TECU)

## Slide 9: Effect on GNSS Observations
Pseudorange is longer – “group delay”
Carrier Phase is shorter – “phase advance”
I in m
TEC in el/m2
f in Hz

## Slide 10: Effect on GNSS Observations

## Slide 11: Calculate Ionosphere Free Pseudorange

## Slide 12: Ionosphere-free Pseudorange
Ionosphere-free pseudoranges are more noisy than individual pseudoranges.
99% correct
≈

## Slide 13: Estimating the Ionospheric Delay
Where frequencies are expressed in Hz, pseudoranges are in meters, and TEC is in electrons/m2

## Slide 14: IONOSPHERIC ZENITH DELAY
The total or slant ionospheric delay depends on the length of the ray path through the ionosphere and how active the ionosphere is in the region it is passing through.
To compare the activity levels the total delay can be approximated as the product of a zenith delay and a geometrical obliquity factor which depends on the satellite zenith angle (compliment of the elevation angle).
Zenith delay is modeled as applying to an observer on the surface of the Earth directly below the IP (ionospheric pierce point) shown by the blue dot in the figure
GPS measurements at stations around the globe are used to observe TECV

## Slide 15: Vertical Delay & Vertical Total Electron Content (TECV)
The TEC along the path for a satellite at zenith angle z, is related to the vertical TEC by the geometrical obliquity factor:
Iono zenith delay (Iz) ~ 1-3 m at night, 5-20 m or more mid-afternoon
OF ranges from 1 (z=0) to ~3 (z=85 deg)
1 TECU ~ 0.16 m

## Slide 16
Global Ionospheric Maps
Global Ionospheric Maps (GIMs) are generated using data from carefully sited GPS receivers (JPL network shown at right).
Generated by:
  JPL (NASA, California)
  Center for Orbit Determination (CODE, U. of Bern, Switzerland)
  GSD, Canada
  UPCG
  Others
Updated (at least) daily, used for GPS and research applications
Calculates TECV from ranging error
Images courtesy NASA/JPL

## Slide 17: TECV Maps
2-hourly snapshots of the Earth's TEC (01:00, 03:00, etc)
Dark blue indicates low TEC and red indicates high TEC (up to 75 TECU ).

## Slide 18: Global Ionospheric Maps (TECV)
http://iono.jpl.nasa.gov/

## Slide 19: Ionospheric Storms
Solar activity such as flares and coronal mass ejections often produce large variations in the particle and electromagnetic radiation incident upon the earth.

## Slide 20
Drivers

## Slide 21: Klobuchar Model – Broadcast Model
Representation of zenith delay:
t is local time at the ionospheric pierce point, expressed in geomagnetic coordinates
A1 – A4 are computed from the a’s and b’s in the nav message
The obliquity factor is approximated as:
50-70% correct

## Slide 22: Klobuchar Model
From Misra & Enge: Figure 5.10
A3
A1

## Slide 23: Where is the Klobuchar Model stored?
2 NAVIGATION DATA RINEX VERSION / TYPE
CCRINEXN V1.6.0 UX CDDIS 14-OCT-07 02:51 PGM / RUN BY / DATE
IGS BROADCAST EPHEMERIS FILE COMMENT
0.1118E-07 0.0000E+00 -0.5960E-07 0.0000E+00 ION ALPHA
0.9011E+05 0.0000E+00 -0.1966E+06 0.0000E+00 ION BETA

## Slide 24: WAAS (Wide Area Augmentation System)
~90-95% correct; guaranteed 7.6 m, actual ~ 1 m accuracy
WAAS supplies correction parameters for a number of points (organized in a grid pattern) across the WAAS service area.
Data are collected from Air Traffic Control centers
For each satellite observation the user receiver interpolates to its pierce point location based on the four closest grid points
Receiver then calculates total delay based on measured delays, using interpolation
Images taken from www.nstb.tc.faa.gov (public domain)

## Slide 25: US Space Weather Center Center – Right Here in Boulder
http://www.swpc.noaa.gov/ustec/index.html

## Slide 26
Quiet
Disturbed
TEC

## Slide 27: Ionospheric Scintillation
Rapid variations in the phase and amplitude of a radio signal that has passed through the ionosphere
Caused by small scale variations in the ionospheric plasma density
Described by S4 intensity-scintillation index: standard deviation of the intensity normalized by the mean intensity.
Primary influence on GPS is the potential for receiver tracking loops to lose lock on the signal.
Seo, et al.
http://waas.stanford.edu/~wwu/papers/gps/PDF/SeoIBSS07.pdf

## Slide 28: SUMMARY OF IONOSPHERIC EFFECTS
Region of the Earth's atmosphere from ~ 100 to ~ 1000 km above the Earth's surface which includes active electrons
Term describing it: total electron content (TEC).
Depends on: Time of day (where the sun is), Season, Latitude, Solar (Sunspot) Cycle
Delay on L1 (m) is approximately 40.3 TEC/f12
Delay on L2 (m) is approximately 40.3 TEC/f22
Corrected in the receiver by dual frequency measurements or the Klobuchar model.
Severe scintillation can cause receivers to lose lock. Not a very common occurrence.

## Slide 29: LINKS
http://www.swpc.noaa.gov/ustec/index.html
http://www.cx.unibe.ch/aiub/ionosphere.html