## Slide 1: Signal Structure - Summary
ASEN 5090
ASEN 5090 LECTURE NOTES – LARSON, AXELRAD
Courtesy He Lin, University of Colorado

## Slide 2: Outline
L1 and L2 carriers
PRN Codes, CDMA, BPSK
Navigation Message
Correlation properties
Spectrum
Signal power
Reading Assignment
  Ch 2, problems 2-1 and 2-2 (See assignment page)
Questions to think about
  What features of GPS are enabled by the codes?
  Why 2 frequencies?
  Would there be an advantage to substantially increasing the GPS signal power? Any downsides?

## Slide 6
Extra Credit
Engineering isn’t just about building something to do a job.
It is about understanding (predicting) how well that job will be done.
Goal of the next homework is to predict how well you can determine your position.

## Slide 7: SIGNAL COMPONENTS
Base frequency is f0 = 10.23 MHz = 10,230,000 Hz (cycles/sec)
L1 = 154 f0 = 1575.42 MHz
L2 = 120 f0 = 1227.6 MHz
C/A code chip rate = f0 /10 = 1.023 Mcps (MHz), 1 ms long
P code chip rate = f0 = 10.23 Mcps (MHz), 37 weeks long, each satellite gets a 1 week segment
Navigation Data rate = 50 bps, 20ms per bit, 6 s per frame, 30 s for individual satellite data, 12.5 min for all

## Slide 8: PROPERTIES OF CODES
Protect against interference
Reduce noise effects
Permit many signals to be transmitted at the same frequency without interfering (known as : code division multiple access - CDMA)
Permit high resolution ranging
Enable communications security (known as : low probability of detection - LPD)
Key characteristics of codes are their type, length, chip rate.

## Slide 9: PRN CODES (pseudo random noise codes)
In GPS, a pseudo random noise code used to modulate a carrier tone
Types of modulation: amplitude (AM), frequency (FM), phase (PM)
Leick, GPS principles
9

## Slide 10: PRN CODES (pseudo random noise codes)
GPS uses BPSK - (Biphase phase-shift keying) sequence of "1's" and 0's" that specify when phase of carrier should be reversed (1) or left alone (0).
Can consider as a sequence of 0's and 1's or 1 and -1's
  In terms of phase-shift keying, 0 corresponds to "don't shift" and 1 corresponds to "shift"
  In terms of digital amplitude modulation, multiplying by a "1" leaves the carrier alone (i.e don't shift) and multiplying by a "-1" inverts it (i.e. shifts it by 180 deg).
These codes enable a GPS receiver to measure the transit time of a signal from a GPS satellite to the receiver antenna.
Reference - Spread Spectrum Systems, Robert C. Dixon, Wiley 1984.
10

## Slide 11: GPS C/A CODES (From Misra & Enge, Problem 2.1)
11

## Slide 12: NAVIGATION MESSAGE (from Misra & Enge)
Misra & Enge Fig. 4.13
12

## Slide 13: SIGNAL SPECTRUM
What frequencies are present in the signal
13

## Slide 14: LEGACY GPS SPECTRUM
PRN codes have a sinc2 spectrum
Main lobe is 2x chipping rate
Side lobes are 1x chipping rate
Power density is very low
14

## Slide 16: SIGNAL POWER
GPS Satellites transmit 27W toward the earth
GPS Signal level on the ground:
  L1 C/A: -158.5 dBW ~10-16 Watts
  L1 P(Y): -161.5 dBW
  L2 P(Y): -164.5 dBW
Spread spectrum signal is “sub-thermal” or below the noise floor
After correlation in the receiver the recovered or despread carrier is above the noise (typical SNR’s 6-15 dB).
Processing gain for spread spectrum is signal BW/ data BW
dB
16

## Slide 17: GPS LEGACY SIGNAL GENERATION
C/A CODE 1.023 Mcps
NAVIGATION DATA 50 bps
P(Y) CODE 10.23 Mcps
L2 CARRIER 1227.6 MHz
L1 CARRIER 1575.42 MHz
90 deg shift
S
S
17

## Slide 18: What Next?
Frame Orbits Clocks
Etc.

## Slide 19: What Next?
What about the Constellation
The Frame Orbits Clocks
Etc.