## Slide 1: Signal Structure
ASEN 5090
ASEN 5090 LECTURE NOTES – LARSON, AXELRAD
Courtesy He Lin, University of Colorado

## Slide 2: Outline
L1 and L2 carriers
PRN Codes, CDMA, BPSK
Navigation Message
Correlation properties
Spectrum
Signal power
Reading Assignment
  Ch 2, problems 2-1 and 2-2 (See assignment page)
Questions to think about
  What features of GPS are enabled by the codes?
  Why 2 frequencies?
  Would there be an advantage to substantially increasing the GPS signal power? Any downsides?

## Slide 3: SIGNAL COMPONENTS
Base frequency is f0 = 10.23 MHz = 10,230,000 Hz (cycles/sec)
L1 = 154 f0 = 1575.42 MHz
L2 = 120 f0 = 1227.6 MHz
C/A code chip rate = f0 /10 = 1.023 Mcps (MHz), 1 ms long
P code chip rate = f0 = 10.23 Mcps (MHz), 37 weeks long, each satellite gets a 1 week segment
Navigation Data rate = 50 bps, 20ms per bit, 6 s per frame, 30 s for individual satellite data, 12.5 min for all

## Slide 4: PROPERTIES OF CODES
Protect against interference
Reduce noise effects
Permit many signals to be transmitted at the same frequency without interfering (known as : code division multiple access - CDMA)
Permit high resolution ranging
Enable communications security (known as : low probability of detection - LPD)
Key characteristics of codes are their type, length, chip rate.

## Slide 5: PRN CODES (pseudo random noise codes)
In GPS, a pseudo random noise code used to modulate a carrier tone
Types of modulation: amplitude (AM), frequency (FM), phase (PM)
Leick, GPS principles
5

## Slide 6: PRN CODES (pseudo random noise codes)
GPS uses BPSK - (Biphase phase-shift keying) sequence of "1's" and 0's" that specify when phase of carrier should be reversed (1) or left alone (0).
Can consider as a sequence of 0's and 1's or 1 and -1's
  In terms of phase-shift keying, 0 corresponds to "don't shift" and 1 corresponds to "shift"
  In terms of digital amplitude modulation, multiplying by a "1" leaves the carrier alone (i.e don't shift) and multiplying by a "-1" inverts it (i.e. shifts it by 180 deg).
These codes enable a GPS receiver to measure the transit time of a signal from a GPS satellite to the receiver antenna.
Reference - Spread Spectrum Systems, Robert C. Dixon, Wiley 1984.
6

## Slide 7: CORRELATION FUNCTION Rxy(τ)
Correspondence between a code and a phase-shifted replica of another code
Cross correlation – correspondence between different codes: Rxy(τ)
Autocorrelation - correspondence of code w/phase shifted version of itself Rx(τ)
Simple idea: Compare shifted code replica with the original reference. Number of bits which agree minus the number of bits which disagree is the correlation.
Note: these equations should be NORMALIZED.
7

## Slide 8: CORRELATION CALCULATION - EXAMPLES
100111101110100010011011111111101
000010001010011100001110010010001
Every time the numbers agree, add 1.
Every time the numbers disagree, subtract 1.
8

## Slide 9
This example: codes for 2 different satellites
100111101110100010011011111111111
000010001010011100001110010010001
14 agree
19 disagree
Total score: -5
Perfect agreement would be 33
9

## Slide 10
01100010101011001000100100000110000011110000
11000101010110010001001000001100000111100001
01100010101011001000100100000110000011110000
11000101010110010001001000001100000111100001
Agreement is perfect
But if you recognize they are shifted by 1:
This example: same satellite codes, but shifted
Not so good - score of -3.

## Slide 11: CALCULATING AUTOCORRELATION(τ)
SHIFT | CODE | AGREE | DISAGREE | AUTOCORRELATION
REF | 1110010 | - | - | -
0 | 1110010 | 7 | 0 | 7
1 | 0111001 |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
11

## Slide 12: CALCULATING AUTOCORRELATION(τ)
SHIFT | CODE | AGREE | DISAGREE | AUTOCORRELATION
REF | 1110010 | - | - | -
0 | 1110010 | 7 | 0 | 7
1 | 0111001 | 3 | 4 | 
2 | 1011100 | 3 | 4 | 
3 | 0101110 | 3 | 4 | 
4 | 0010111 | 3 | 4 | 
5 | 1001011 |  |  | 
6 | 1100101 |  |  | 
7 | 1110010 |  |  | 
12

## Slide 13: GENERATING PRN CODES
Tapped feedback shift register
Epoch state
XOR Logic Table
A | B | Y
0 | 0 | 
1 | 0 | 
0 | 1 | 
1 | 1 | 
13

## Slide 14: GENERATING A CODE
Example: Generate the PRN code for a 3 stage shift register tapped at [3,2] starting from an all ones state. (The PRN Code is made up of the third stage bit values.)
Shift | Stage |  |  | Code
T | 1 | 2 | 3 | 
0 | 1 | 1 | 1 | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
14

## Slide 15: GENERATING A CODE
Example: Generate the PRN code for a 3 stage shift register tapped at [3,2] starting from an all ones state. (The PRN Code is made up of the third stage bit values.)
Shift | Stage |  |  | Code
T | 1 | 2 | 3 | 
0 | 1 | 1 | 1 | 
1 | 0 | 1 | 1 | 1
2 | 0 | 0 | 1 | 1
3 | 1 | 0 | 0 | 1
4 | 0 | 1 | 0 | 0
5 | 1 | 0 | 1 | 0
6 | 1 | 1 | 0 | 1
7 | 1 | 1 | 1 | 
15

## Slide 16: MAXIMAL LENGTH CODES
Maximal length codes are the longest codes that can be generated by a given number of shift register stages. For an n-stage shift register, the longest code is 2n - 1 chips (i.e. 1's or 0's). Maximal length codes have many interesting properties, especially their autocorrelation function.
For a maximal length code, the autocorrelation function for a phase shift other than 0 or (2n - 1) is -1. For any code, the autocorrelation for a 0 shift is equal to the number of chips in the code.
16

## Slide 17: Why is maximal length code 2n -1?
17

## Slide 18: GPS C/A CODES (From Misra & Enge, Problem 2.1)
18

## Slide 19: PRN 5 CODE SEQUENCE
19

## Slide 20: Autocorrelation of PRN 5 C/A Code
20

## Slide 21: Computing a cyclic correlation
function P = cyc_corr(x,y)
% Function to compute the cyclic correlation
% for ASEN 5090
% P. Axelrad, University of Colorado, 9/2009
%
% define the inputs! What do they mean?
Y = [y y y]'
n = length(x)
for i = 1:2*n % sweep the lag from –n to + n
Rxy(i) = x*Y(i:i+n-1);
lag(i) = i-1-n;
end
plot(lag,Rxy),grid,xlim([-n n])
xlabel('LAG'),ylabel('CORRELATION')
21

## Slide 22: Cross correlation between shifted PRN5 & reference PRN 5
yshifted = [y(101:1023) y(1:100)];
P = cyc_corr(yshifted,y);
22

## Slide 23: IMPACT OF CORRELATION PROPERTIES
What makes a useful code?
  For ranging:
  For CDMA:
  For acquisition:
23

## Slide 24: NAVIGATION MESSAGE (from Misra & Enge)
Misra & Enge Fig. 4.13
24

## Slide 25: SIGNAL SPECTRUM
What frequencies are present in the signal
25

## Slide 26: LEGACY GPS SPECTRUM
PRN codes have a sinc2 spectrum
Main lobe is 2x chipping rate
Side lobes are 1x chipping rate
Power density is very low
26

## Slide 28: SIGNAL POWER
GPS Satellites transmit 27W toward the earth
GPS Signal level on the ground:
  L1 C/A: -158.5 dBW ~10-16 Watts
  L1 P(Y): -161.5 dBW
  L2 P(Y): -164.5 dBW
Spread spectrum signal is “sub-thermal” or below the noise floor
After correlation in the receiver the recovered or despread carrier is above the noise (typical SNR’s 6-15 dB).
Processing gain for spread spectrum is signal BW/ data BW
dB
28

## Slide 29: DECIBELS
RdB = 10 log10 (R)
29

## Slide 30: GPS LEGACY SIGNAL GENERATION
C/A CODE 1.023 Mcps
NAVIGATION DATA 50 bps
P(Y) CODE 10.23 Mcps
L2 CARRIER 1227.6 MHz
L1 CARRIER 1575.42 MHz
90 deg shift
S
S
30